## Slide 2
ATLAS эксперимент
Научная сессия ученого совета ОФВЭ ПИЯФ
24-27 декабря 2012 года
Олег Федин
Notes: ё

## Slide 3: Содержание
Status of the ATLAS detector.
Performance of the ATLAS detector:
  to highlight the PNPI’s participation for the further improvement and control of the ATLAS performance.
PNPI participation in ATLAS:
  physics program;
  detector development;
  TDAQ/DCS.
PNPI plans for ATLAS upgrade.

## Slide 4: p-p integrated luminosity vs time
Peak luminosity seen by ATLAS: ~ 7.73 x1033 cm-2 s-1
LHC records in 2012 (in brackets results for 2011)
Maximum luminosity delivered in one fill 237.32 pb-1 (122.44)
Maximum luminosity delivered in one day 286.33 pb-1 (135.45)
Maximum colliding bunches (design 2808) 1380 (1854)
Maximum bunch population (design 1.15 1011) ~2.0 1011 (1. 1011)
Bunch spacing (design 25 ns) 50 ns
Maximum peak events per bunch crossing 71.55 (33.96)
Longest time in stable beam foe one fill 22.8 hours (26)
Time in stable beam 73 days out of 259 days of LHC works (28.4%) (2011 23.5%)
Total integrated luminosity in 2012
ICHEP,4 of July ~ 5 fb-1
Higgs discovery
Number of events in full 2010-2012 dataset (~ 25 fb-1) after all selection cuts:
W  lν ~ 100 M (LEP2: 0.2M pair W+/W-)
Z ll ~ 10 M (LEP 16M )
tt  l+X ~ 0.4 M
SM Higgs ~ 400
[~1 H γγ (~1 H 4l) produced every 50’ (14h)
at 7x 1033 ]

## Slide 5: Multiple pp-collisions per bunch crossing
Zμμ from 2012 data with 25 reconstructed vertex
(only tracks with pT>20 GeV and #Si hits >9 shown)
The BIG challenge in 2012: PILE-UP
Experiment’s
design value
(expected to be
reached at L=1034 !)
Zμμ
Peak interaction per bunch crossing
2011: <μ>=9
2012: <μ>=20
Mean # of interaction per crossing

## Slide 6: Detectors operation
Fraction of non-operational detector channels:
(depends on the sub-detector) few permil to 3.5%
Data-taking efficiency = (recorded lumi)/(delivered lumi): 93.7% (2011 -93.5%)
Good-quality data fraction, used for analysis : (depends on the analysis) : 90-96%
93.7%
TRT
97.5%

## Slide 7: Trigger operation
L1: up to ~ 65 kHz
L2: up to ~ 5 kHz
EF: ~ 400Hz
Note > 550 items in trigger menu
Managed to keep inclusive un-prescaled lepton thresholds within ~ 5 GeV over last two years in spite of the factor ~70 peak luminosity increase
Optimization of selections (e.g. object isolation) to maintain low un-prescaled thresholds (e.g. for inclusive leptons) in spite of x2 higher luminosity and pile-up than in 2011
Pile-up robust algorithms developed (~flat performance vs pile-up, minimize CPU usage, ...)
Results from 2012 operation show trigger is coping very well (in terms of rates, efficiencies, robustness, ..) with harsh conditions while meeting physics requirements
Item | pT threshold (GeV) | Rate (Hz) at 5x1033
Incl. e | 25 | 70
Incl. µ | 24 | 45
ee | 12 | 8
µµ | 13 | 5
ττ | 29,20 | 12
γγ | 35,25 | 10
ETmiss | 80 | 17
Lowest un-prescaled thresholds
(examples)

## Slide 8: Electrons
e24vhi_medium1 OR e60_medium1
Efficiency of inclusive electron trigger (ET thresholds as low as 24) as a function of “pile-up”
From Z ee events
Stability of EM calorimeter response vs time
(and pile-up) during full 2012 run better than 0.1%
Present understanding of calorimeter E response
(from Z, J/ψ  ee, W eν
data and MC):
E-scale at mZ known to ~ 0.3%
Linearity better than 1% (few-100 GeV)
“Uniformity” (constant term of resolution): ~ 1% (2.5% for 1.37<|η|<1.8)
Efficiency of inclusive electron trigger as a function of ET
Mas resolution ~ 1.83 GeV (2%)
2012 Zee mass peak

## Slide 9: Electrons
High efficiency for low-pT electrons (affected by material) crucial for H 4e, 2μ2e
Improved track reconstruction and fitting to recover e± undergoing hard Brem achieved ~ 98% reconstruction efficiency, flatter vs η and ET
Results are from Z ee data and MC
tag-and-probe
Re-optimized e± identification using
pile-up robust variables (e.g. Transition
Radiation, calorimeter strips)  achieved
~ 95% identification efficiency, ~ flat
vs pile-up; higher rejections of fakes
PNPI contribution:
software development for the tracks refit to account lost of the energy due to brem
validation of electron reconstruction and identification software
Reconstruction efficiency vs η
Reconstruction efficiency vs ET
<ε>~98%

## Slide 10: Electrons
PNPI contribution: A measurement of the electron identification efficiency using Υe+e- decays by tag&probe method.
Work is supported by RFBR grant in 2012-2013
Special trigger was developed to register decays of the Υe+e-: 2 legs L1 EM clusters, one high-pT (ET>16 GeV), one at low pT (ET>6 GeV), tight ID for high pT cluster and no requirement for track matched to low pT cluster, invariant mass of two electrons between 6 and 20 GeV.
For the tag electrons applied tight ID selection.
Efficiency of probe electrons measured in the data and MC.
Scale Factors defined as εdate/εMC and used to correct MC prediction
2 electron invariant mass (no ID requirements for probe electrons)
2 electron invariant mass (loose ID requirements for probe electrons)
Υ(1S):
9.460 GeV
Υ(2S):
10.023 GeV

## Slide 11: Photon
Trigger | Physics use | Rate (Hz) at 7x1033
1γ: ET>120 GeV, ID-loose | Multi | 12
2γ:ET>35(25) GeV, ID loose | Higgs | 14
2γ: ET>20 GeV, ID-medium | SM | 5
3γ:ET>15 GeV, ID loose | SM tri-booson | 1
2012 unprescaled photon triggers
Trigger efficiency vs pT
ID efficiency vs ET
Converted γ
ID efficiency vs ET
Unconverted γ
ID efficiency vs “pileup”
Unconverted γ
From Z eeγ events
PNPI contribution:
validation of software for photon reconstruction and identification

## Slide 12: Muons
~ 2M Z μμ
Mass
resolution
~ 2 GeV
2012 Z μμ mass peak
Muon trigger efficiency
end-cap
Reconstruction efficiency ~ 97%,
~ flat down to pT ~ 6 GeV and over |η|~2.7
Reconstruction efficiency stable to pile-up

## Slide 13: Missing ET
Understanding of Etmiss (most sensitive to pile-up) is crucial for H WW(*)  lνlν ,
W/ZHW/Zbb, Hττ
Number of reconstructed primary vertices
Offline ET miss (GeV)
Many improvements in ET miss trigger: e.g. pile-up suppression, L2 fast front-end board sums instead of L1 only  same threshold as in 2011, sharper turn-on curve
ETmiss resolution vs pile-up and vs ΣET in Z μμ events before and after pile-up suppression using tracking information
PNPI contribution:
Control Etmiss egamma trigger efficiency using data.
Support and development of the HLT trigger software.
2012 Z μμ

## Slide 14: Search for high-mass resonances decaying to dileptons
Expect very high-pT electrons from this signal
ET>25 GeV |η| < 2.47, excluding crack 1.37<|η| < 1.52
Cuts on shower shape and track matching
A hit in the first layer of the pixel detector is required if to suppress background from photon conversions
Higher ET must be isolated requiring ΣET (ΔR < 0.2) < 7 GeV – to supress QCD background
2 electrons invariant mass
No statistically significant excess above the Standard Model expectation is observed;
Upper limits are set at the 95% CL on the cross section times branching fraction of Z′ resonances decaying into l+l− pairs as a function of the resonance mass.
As a result, Z′ bosons of the Sequential Standard Model with masses less than 2.47 TeV are excluded at 95% CL.
Z* bosons with masses less than 2.20 TeV are excluded at 95% CL (only 2011 data)
Several models predict new resonances decaying to pairs of charged leptons or into lepton:
Spin-1 benchmarks: Z’ in Sequential Standard Model or E6 grand unified symmetry
Spin-2 benchmark: Graviton in Randall-Sundrum models
Chiral spin-1 bosons (M.V.Chizov Phys. Atom. Nucl. 71, 2096 (2008))

## Slide 15: Search for high-mass resonances decaying to lepton and neutrino
mT transverse mass
Etmiss missing transverse energy
120 GeV
No yet new limits are set in 2012 data.
In 2011 data no statistically significant excess above the Standard Model expectation is observed;
Upper limits are set at the 95% CL on the cross section times branching fraction of W’′ resonances decaying into l+l− pairs as a function of the resonance mass.
As a result, W′’ bosons of the Sequential Standard Model with masses less than 2.5 TeV are excluded at 95% CL.
W* bosons with masses less than 2.38 TeV are excluded at 95% CL.

## Slide 16: TRT eFastOR trigger
TR: photon (soft X-ray emitted by a charge particle when traversing the boundary between materials with different dielectric constants
Goal is to build an enhancement to the current TRT FastOR Level-1 Trigger system that will significantly increase ATLAS sensitivity to highly ionizing particles (HIPs), such as magnetic monopoles and Q-balls.
Trigger should run within ATLAS Level-1 trigger.
eFastOR trigger takes advantage of differences in High Threshold (HT) signals from the TRT produced by known particles compared to those produced by HIPs.
5% acceptance for monopole
Work is supported by Min Of Sci.

## Slide 17: Ultrasonic vapour analyzer/flowmeter for the ATLAS silicon tracker
Sound velocity vs % concentration of C3F8/N2 mixture
The vapour flow rate is calculated from the sound transit times measured parallel, tdown, and anti-parallel, tup, to the flow direction, according to the following algorithm:
c = L/2 * ((tup + tdown)/ tup* tdown
Mixture precision:
  ~0.3% for C3F8/C2F6
  < 10-4 for N2/C3F8
Flow resolutions of ± 2% F.S. for flows up to 250 l.min-1,
± 1.9% F.S. for linear flow velocities up to 15 ms-1
View of the electronics for Utrasonic amalyzer installed in the ATLAS pit

## Slide 18: Pixel Service Quarter Panels (SQP)
Transfer services from outside world to pixel detectors
Problematic opto-couplers on SQP
To replace these need new infrastructure and electronics
Mew electronics will allow greater readout bandwidth for > 1034 operation
PNPI technicians are participating in creation of the SQP

## Slide 19: TDAQ/DCS
Development and maintenance of the ATLAS data acquisition (TDAQ) system control and monitoring software at Point 1: system configuration, debugging, new features development.
TDAQ s/w release validation, maintenance (patching), s/w installation at P1, maintenance of TDAQ online infrastructure.
Development and deployment of a new automation tool “Shifter Assistant” used by TDAQ and ATLAS subdetectors at P1.
Expert (level 1,2 on-call) support for the running system at P1.
Shifts at P1: manning the Run Control desk.
  Administering and Technical support of OS Windows on DCS PCs (> 100).
  Support and improvements of:
        Rack Control system,
        DCS Access Control (including remote access),
        ATLAS – LHC Communication Interface
        Interface to Condition Database,
        CANopen OPC server – Front-end interface used by all LHC experiments.
      New development for LHC/ATLAS Upgrade
        CANOpen OPC server in advanced standard OPC UA.
      DCS Expert on-call (7/7,24/24) ~25 weeks/year.
TDAQ Shifter assistance
TDAQ PNPI contribution :
DCS PNPI contribution :
Отдел информационных технологий проф. Рябов Ю.Ф.

## Slide 20: Plans for LHC Upgrade
?, IR
4x
, bunch spacing 25 ns
~20-25 fb-1
~75-100 fb-1
~350 fb-1
, bunch spacing 25 ns
, bunch spacing 50 ns
Go to design energy, nominal luminosity
Injector and LHC Phase-1 upgrade to ultimate design luminosity
HL-LHC Phase-2 upgrade, IR, crab cavities?
√s=14 TeV, L=5x1034 cm-2 s-1, luminosity levelling
√s=14 TeV, L~2x1034 cm-2 s-1, bunch spacing 25 ns
√s=13~14 TeV, L~1x1034 cm-2 s-1, bunch spacing 25 ns
√s=7~8 TeV, L=6x1033 cm-2 s-1, bunch spacing 50 ns
LHC startup, √s = 900 GeV
Towards to High Energy LHC (HE-LHC) -√s=33 TeV

## Slide 21: ATLAS upgrade

## Slide 22: New Muon Small Wheels
Existing Small Muon Wheels: CSC and MDT (Muon Drift Tubes)
L1 trigger rate for L=3x1034cm-2s-1
 | pT>20 GeV (kHz) | pT>40 GeV (kHz)
w/o NSW | 60 | 29
w NSW | 22 | 10
New Small Muon Wheels: sTGS and Micromegas
Possible participation of PNPI in assembly of sTGC and front-end electronic development.

## Slide 24
Back-up slides

## Slide 25: The MC toy model for BEC
The MC toy model for Bose-Einstein correlations (BEC) has been proposed to make a best choice from different reference distributions. It occurs that the deviation from the model values of the BEC parameters is provided by the reference sample which is being emulated from "observed" sample by the turn of all momenta vectors in the transverse plane by a random angle.
In the case of the experimental data analysis the appropriate choice of the reference sample even more important.
The ATLAS data on multi-particle production with the beam energy 2.76 TeV and 7.0 TeV analyzed with the selected reference samples.
For the first time it is established that the radii of the particles radiation area is not dependent on the multiplicity , i.e. the value is saturated. The value of such radii has to be dependent on the beam energy. To make it more convincing, the data with a special trigger on high multiplicity has to be investigated with different beam energy. This is already done for the 2.76 TeV data. Such special sample is also collected with the beam energy 7 TeV. The analysis is under way.

## Slide 26: TRT performance

## Slide 27: TRT performance
The TRT significantly improves the momentum resolution compared to tracks reconstructed with silicon hits only
Z mass resolution in the Inner Detector shows good performance σ ~ 2.36 GeV.
Good agreement data/MC

## Slide 28
Preliminary HE-LHC - parameters

## Slide 29
Efficiency is defined as the ratio between the annual luminosity target of 250 fb-1 over the potential luminosity that can be reached with an ideal cycle run time with no stop for 150 days: trun= tlev+tdec+tturn. The turnaround time after a beam dump is taken as 5 hours, tdecay is 3 h while tlev depends on the total beam current
baseline
Target parameters for HL-LHC run